000 Water Supply & Distribution

Item 000 The Vadle Curb Box Lock

000.01  Description

000.02  Installation

000.03 Basis of Payment

000.01  Description.  The Contractor is to provide all labor, material and equipment to install The Vadle Curb Box Lock at the locations shown on the plans.

000.02  Installation.  For 1" and 3/4" curb stops and curb boxes installation simply place The Vadle on a properly prepared sub base under the curb stop.  If the anti-twist ring fits over the key of the curb stop then push the ring onto The Vadle until it locks into place (with the 3/4 Mueller Mark II Oriseal make sure the tab on the side of the key is on the side of the centering ring with the cut-out in it and press down until the ring is resting on the curb stop.  The ring will lock onto the curb stop).  If the curb stops has a cone shape design, place the larger end of the valve body in the larger side of The Vadle.  Then place the curb box over The Vadle. Finally backfilling according to the construction specifications for installation of curb stops and curb boxes.

Curb box installations where The Vadle is going to be placed upside down.  The 1" Ford inverted key or a 1" McDonald inverted plug curb stop, simply turn The Vadle upside down and push into the ground securely under the curb stop.  Then set the valve on The Vadle and put the curb box over the valve.  These two curb stops fit securely in the curb box.  The Vadle serves as a stable base and foundation in this application.  Finally backfilling according to the construction specifications for installation of curb stops and curb boxes.

When installing The Vadle on soft or unstable ground The Vadle can be secured to a larger base such as a block or stepping stone.  Simply screw The Vadle down onto a larger base with any form of anchoring screws to create a solid secure foundation.  Next place the curb stop into The Vadle.  Then place the curb box over The Vadle.  Finally backfilling according to the construction specifications for installation of curb stops and curb boxes.

000.03  Basis of Payment.  Payment shall be at the unit price shown in the proposal and shall be complete compensation for providing all work necessary to furnish and install The Vadle Curb Box Lock as covered in these specifications.

Payment will be made at the contract price for:

Item		Unit		Description

000		Each		The Vadle Curb Box Lock